## Slide 1
Sio Silica Corporation’s
Environment Act Project Proposal
- Presentation at the Public Hearing -
Holländer, H.M.; Woodbury, A.D.
PorousTec Ltd.
07.03.2023

## Slide 2: Dr. Hartmut Holländer, P.Eng. (MB)
>20 years of experience across Canada and internationally
2010-2012: regulatory authority (State Authority of Mining, Energy and Geology - Landesamt für Bergbau, Energie und Geologie, LBEG) Hanover, Germany
  State-of-the-art of science and technology: authorized expert for the nuclear waste repository Asse II and research mine Gorleben, Germany (80%)
  State-of-the-art (industry standard): numerical models in environmental proposals, i.e. groundwater withdrawal by waterworks and industry (20%)
2013-2022: University of Manitoba, Department of Civil Engineering, Groundwater Engineering (research assistant, Associate Professor, Professor)
2020- : PorousTec Ltd, Winnipeg, MB, Director
2022- : Ingenieurgesellschaft Dr. Schmidt mbH, Stade, Germany, CEO

## Slide 3: Dr. Allan Woodbury, P.Eng. (MB, BC)
Lifetime Professor Emeritus, Department of Civil Engineering, University of Manitoba
>40 years of experience across Canada and internationally
Considerable experience in service to Manitoba and in the area of question
Provided consultation to more than 16 governments and organizations across North America, including AECL and the Center for Nuclear Waste Regulatory Analyses in Texas

## Slide 4: Outline
Hydrogeological Investigations
Site Conceptual Model
Numerical Groundwater Modeling
Geochemistry

## Slide 5: Overarching Concerns
What is a sustainable amount of water to develop from an aquifer?
Avoid dewatering an aquifer; avoid mining groundwater (discharge from all sources exceeds recharge)
Avoid excessive drawdowns, which cause well interference with other users
Groundwater quality: inducing water of poorer quality into water supply wells
Subsidence, deformation, sink hole collapse; preserving aquifer integrity
Preventing cross contamination between aquifers
Sealing wells and aquifers from surface contamination

## Slide 6: Area of Interest
Study area from Sandilands to Red River (~80 km)
Area of interest (red) in the centre of the study area
~80 km
~40 km
Sandilands recharge area
Start of Carbonate aquifer and Winnipeg Shale
Start of Winnipeg sandstone aquifer
Red River

## Slide 7: Which data are needed to study such a problem?
Landscape features/boundaries
  River, creeks, lakes
  Recharge areas (mainly Sandilands, Birdshill area)
Geology (GWDrill database, additional boreholes)
  Which formations need to be considered?
  Layer thickness
Hydraulic properties of formations
  Hydraulic conductivity
  Storativity
Regional groundwater table maps for specific dates
  generally: steady-state conditions for a certain period (e.g., last 10 years or periods when pumping was minimal)
Wells
  Location
  Pumping rates

## Slide 8: Hydrogeological Investigations (i)
Key question: Was the investigation program adequate?
Size of study area: ~3200 km2 – basin scale
How homogenous (constant in space) is each formation?
  Aquifers: hydraulic properties in horizontal direction
  Aquitards/aquicludes: hydraulic properties in vertical direction
Based on experience and literature reviews, aquifers are not homogeneous.
Testing
  1 aquifer test: industry standard to derive regional data (~1-2 km around borehole)
  5 slug tests: local data (~2 m around borehole) – not suitable for regional investigations

## Slide 9: Hydrogeological Investigations (ii)
Key question: Was the investigation program adequate?
1 aquifer test = assumption is that the aquifers in the project area are homogenous
Aquifer test covers about 3 km2 and the project is about 3,200 km2
It cannot be expected that such a large area is (completely) homogenous
Other studies (e.g., extensive study by Kennedy and Woodbury, 2002) show heterogenous aquifer properties in the study area

## Slide 10: Hydrogeological Investigations (iii)
Key question: Was the pump test adequately performed and evaluated?
Aquifer test: step test followed by constant rate
  Step Test: unusual intervals of (1) 412 to (2) 402 USGPM, to (3) 421 USGPM,
  Constant rate: (4) 372 USGPM
  3 days for pumping (not all observation wells showed steady-state drawdown)
  followed by 4 days of observing the recovery
(1)
(2)
(3)
(4)

## Slide 11: Hydrogeological Investigations (iv)
Key question: Was the pump test adequately performed and evaluated?
All evaluation methods assume confined conditions (= no drawdown should be observed in carbonate aquifer)
Figs. 3-2 & 3-3 show drawdown in the carbonate aquifer (95-8 VW2: ~1.5 m)
Shale aquitard appears to exhibit leaky conditions
Why was this not evaluated using a leaky attempt (hydraulic properties of the Winnipeg Shale)?
Meaning: Is the shale leaky (pervious) or is the shale partially non-existent?
Hydrogeological Assessment Final Report (HAFR p.32): “… this information suggests the Winnipeg shale is an effective barrier to interaction between the two aquifers at this location …”

## Slide 12: Hydrogeological Investigations (v)
Key question: Was the pump test adequately performed and evaluated?
(Horizontal) hydraulic property of the Winnipeg Shale
Pump test: 1.1 x 10-4 m/s
Numerical model (steady-state condition): 3.2 x 10-5 m/s
Numerical model (transient condition): altered, value not clear
Earlier studies: 5.7 x 10-5 m/s e.g., Kennedy and Woodbury, 2002 using a zone approach = heterogeneity)
How to interpret these differences?

## Slide 13: Hydrogeological Investigations (vi)
What questions have not been answered at all?
There are no observations of the vertical hydraulic properties of the Winnipeg Shale in the proposed mining area
What will happen to the aquitards, the aquifers, and their material properties, after the mining activities?
Will water of poorer quality be drawn into zones that are currently good quality?

## Slide 14: Conceptual Model
Which information are critical in a conceptual model?
Analysis of boreholes and create layered 3D system
Definition of the model area and description of boundaries
  Information on regional flow system(s)
Choice of numerical code
Initial choice of layer parametrization (based on data and stratigraphy)
Material properties

## Slide 15: Site Conceptual Model (i)
Layers
  Required: Carbonate aquifer (green), Winnipeg shale (black), Winnipeg sandstone formation (yellow)
  Useful: quaternary sediments (grey)
  additional: Precambrian bedrock (red, no impact on results)

## Slide 16: Site Conceptual Model (ii)
Regional groundwater table maps
Industry standard: Need to be created for a specific date (alternative: short period)
Report: all available data were used so that data from e.g., 1980 might be plotted with data from 2020
HAFR, Fig. 5-11

## Slide 17: Site Conceptual Model (iii)
Boundary conditions
Brackish water exists in the Winnipeg Sandstone Formation near the Red River
Correction of measured hydraulic heads required
HAFR, Fig. 5-11
Betcher et al., 1995
up to 30 g/L TDS

## Slide 18: Site Conceptual Model (iv)
Wells
Are of key interest (water supply)
Aquifer test showed already that Winnipeg Shale is leaky
Kennedy (2002) showed that nearly 500 wells are screened over both aquifers
It is not clear if any (and which) wells in the modeling domain are screened or open over several aquifers
Provincial database of wells and observation wells is generally not in the best conditions (actual data, data uncertainty, e.g., location)

## Slide 19: Site Conceptual Model (v)
Choice of numerical code
FEFLOW is an adequate model to solve such problems
HAFR mentions that the movement of saline waters: “… even this small volume of water could dramatically affect local quality over time”.
Single-phase simulation does not reflect brackish groundwater in the study area
Transient simulation
  Which data points are available at time t = 0 (initial conditions)?

## Slide 20: Groundwater Modeling
What is a groundwater model?
Simplified, schematic representations of a part of the hydrogeological system regarding to selected properties and processes for a groundwater body
Primarily used for hydrogeologic prediction and for understanding hydrogeologic processes
Other uses:
Interpretation and synthesis of observed data
Calculating data for non-observed points (monitoring wells are expensive)
Hydraulic heads are observable, flux has to be calculated
Extrapolating/predicting future states
Calculating variants to pick the best solution

## Slide 21: Numerical Groundwater Modeling (i)
Objectives (HAFR):
Evaluation of the potential for the project to impact
Groundwater quantity
Quality
Users of the surface and groundwater in the area
Missing topics:
Details on evaluation criteria
Subsidence and potential pathways opening up through the limestone aquifer

## Slide 22: Numerical Groundwater Modeling (ii)
Calibration process
Calibration: adjustment of the model by variation of parameters within reasonable bounds
  steady-state: groundwater measurements based on mixed dates
  transient: aquifer test (total length of 7 days)
Validation: simulation of other test days or different time periods for testing of the ability to predict – not carried out
Sensitivity analysis: Identification of uncertainties by variation of the model parameter

## Slide 23: Risk of Oversimplified Models
Equifinality
If system parameters are underrepresented, a large number of solutions is possible, e.g.,
K1 = 8x10-5 m/s
K2 = 2x10-4 m/s
recharge: 200 mm/a
hobs
hsim
K1 = 4x10-5 m/s
K2 = 1x10-4 m/s
recharge: 100 mm/a
hobs
hsim
Solution: More data are required!

## Slide 24: Numerical Groundwater Modeling (iii)
Calibration (steady-state)
Systematic overestimation for heads below 275 m asl
Also visible by
Model calibration not to industry standard
Model does not represent behavior of the natural groundwater flow
Model cannot be used as a predictive tool at this point

## Slide 25: Numerical Groundwater Modeling (iv)
Calibration (transient)
Drawdown in Carbonate aquifer often lower than observed (Winnipeg Shale)
Initial drawdown often does not follow the observed data (storativity)

## Slide 26: Numerical Groundwater Modeling (v)
Calibration (transient)
Hydraulic conductivity, storativity, and recharge rates were modified to match observations from the actual pump test.
  Not adequate in transient calibration to recalibrate K and recharge
  Statistics of actual final match were not listed
  Sub-optimal fits: distances greater 300 m generally show higher observed drawdown than simulated, and the reverse is true for distances under 300 m
Calibrated values
  Calibrated values were not compared (and discussed) to literature values
  Anisotropy was assumed (10:1) but not evaluated in the model
Scenarios
  Worst-case scenario: Failure of Winnipeg Shale was not considered in HAFR
  Partial consideration in the recent work (we were not able to review it since it was presented last week only)

## Slide 27: Numerical Groundwater Modeling (vi)
Sensitivity
Parameter uncertainty not defined (field test – literature values – (old) driller reports)
Limited sensitivity includes various hydraulic parameters (of the shale layer) were altered by either increasing or decreasing values by a specified amount.
Drawdowns in the Carbonate and Winnipeg Sandstone aquifers are considered to be “moderately sensitive” to changes in K of the Winnipeg Sandstone.
This comment reinforces our conclusion that the hydraulic parameters used in the numerical modeling need to be re-examined.
No boundary conditions (besides recharge) were included

## Slide 28: Geochemistry (i)
Review related to acid-mine drainage
Does not include that changes to the flow, pH, and redox conditions within the aquifer due to the mining activities could result in leaching of trace metals into the aquifers (e.g., Bru121-1_36.57 to 37.00, Winnipeg Shale)
Leaching from surface water to groundwater not considered and was not compared to the guidelines
Potential pathways are sinkholes in the Upper Carbonate (e.g., near Beausejour) and brownfields

## Slide 29: Geochemistry (ii)
We heard last week:
Assumption:
just 1% waste rock - expected annual production 1,360,000 m3 result in waste rock of 1,360 m3 (~2,100 tonnes)
5 years: 10,500 tonnes plus cuttings from drilling (roughly 1000 boreholes)
Sampling
Not many samples: 9 rock samples related to acid mine drainage taken
Not a single duplicate (uncertainty range?)
Unqualified grab samples taken from Winnipeg Sandstone formation
Documentation partly not adequate (e.g., what happened during storing water sample BRU 96-1 between collection and delivery to ALS?)

## Slide 30: Geochemistry (iii)
Geochemical sampling before, during, and after the pumping test does not mimic reinfiltration during mining operation
Key drivers for acid mine drainage such as dissolved oxygen (DO), pH need to be stronger considered in terms of geochemical changes
Assumption: groundwater at 6˚C -> 12,45 mg/L; process might allow for 40% saturation -> DO = 5 mg/L
Slurry could be pumped 2:1 (fluid : sand, Sio says 1:1) -> 21,000 tonnes of silica sand need ~28,000 m3 of water -> total DO introduction 70 kg for each cluster
Though not all will stay in the Winnipeg Sandstone formation this has the potential to change the redox state drastically
This is not included in any evaluation

## Slide 31: Geochemistry (iv)
Geochemical Modeling – Open Questions
Trace metals, which are contaminants of concern for drinking water quality, not considered
Modelling selected only low-risk scenarios and did not seek to address two major issues - a reduced water quality in general, or risk to human, aquatic, or agricultural life. Risks were not identified, e.g., by worst-case scenarios (e.g. data based on sample Bru121-1_36.57 to 37.00).
Geochemical models are not fully described, e.g., redox conditions (pe) are missing, or is pe = default = 4 used?
Potential changes to the groundwater chemistry due to the expected changes in pH and redox conditions are not included

## Slide 32: Thank you very much for your attention!

## Slide 33: References
Betcher, R., Grove, G., Pupp, C., 1995. Groundwater in Manitoba: hydrogeology, quality concerns, management, Environmental Sciences, Division National Hydrology Research Institute, Environment Canada.
Ferguson, G., Betcher, R.N., Grasby, S.E., 2007. Hydrogeology of the Winnipeg Formation in Manitoba, Canada. Hydrogeology Journal, 15(3): 573-587.
Kennedy, P.L., 2002. Groundwater Flow and Transport Model of the Red River/Interlake Area in Southern Manitoba, University of Manitoba, Winnipeg, MB.
Kennedy, P.L., Woodbury, A.D., 2002. Geostatistics and Bayesian updating for transmissivity estimation in a multiaquifer system in Manitoba, Canada. Ground Water, 40(3): 273-83.
Kennedy, P.L., Woodbury, A.D., 2005. Sustainability of the Bedrock Aquifer Systems in South-Central Manitoba: Implications for Large-Scale Modelling. Canadian Water Resources Journal / Revue canadienne des ressources hydriques, 30(4): 281-296.
Phipps, G., Betcher, R.N., Wang, J., 2008. Geochemical and Isotopic Characterization of a Regional Bedrock/Surficial Aquifer System, Southeastern Manitoba, GeoEdmonton ’08.
Wang, J., Betcher, R.N., Phipps, G.C., 2008. Groundwater Resource Evaluation in Southeastern Manitoba, GeoEdmonton ’08.